## Slide 1
Network Slicing
How one physical network becomes many virtual networks
Advanced Networks Research Lab · UT Dallas · 2026
Network Slicing
Elastic Traffic
Admission Control

## Slide 2
Seminar Roadmap
One hour. Six topics. By the end you will understand how a cell tower, a streaming app, and a self-driving car can all share one network — without stepping on each other.
01
The Modern Internet
Bandwidth, latency, and why one-size-fits-all fails
02
Virtualization & NFV
Decoupling software from hardware
03
Network Slicing
Isolated virtual networks on shared infrastructure
04
Service Function Chains
Ordered pipelines of network functions
05
Elastic Traffic
Demand that fluctuates between base and peak
06
Lab Work
RL-based admission control for elastic slices

## Slide 3
Part 1: The Modern Internet
Why simple "best-effort" delivery is no longer enough

## Slide 4
The Internet Carries Wildly Different Traffic
Every application has a different relationship with bandwidth, delay, and reliability — and they all share the same wires.
4K Video
Streaming
Needs 25 Mbps sustained. Can tolerate 2–3 sec buffering delay. Does not need guaranteed timing.
Video Calls
Needs only ~1 Mbps — but any delay >150 ms or jitter causes garbled audio/video.
Hospital IoT
& Alarms
Very low data rate. But a missed alarm packet can cost a life — reliability is paramount.
Autonomous
Vehicles
Needs < 1 ms round-trip latency to react to obstacles. Also needs guaranteed bandwidth for sensor fusion.
Cloud Backup
Huge bursts of data (gigabytes) on a schedule. No timing requirement — just raw throughput.

## Slide 5
Best-Effort vs Quality of Service (QoS)
Traditional IP networks deliver packets on a "best-effort" basis — no guarantees. QoS mechanisms attempt to prioritize, but they are static and hard to manage at scale.
Best-Effort (Traditional)
All packets treated equally
No bandwidth or latency guarantees
Works fine for email & web browsing
Breaks down for real-time applications
Quality of Service (QoS)
Traffic classes get different priorities
Router queues can favor certain packets
Requires manual per-device configuration
Does not scale to thousands of services
What we really need — Network Slicing
Logical isolation: each service runs in its own virtual network with dedicated resources
Guaranteed SLAs (bandwidth, latency, availability) per slice
All slices share the same physical hardware — but are invisible to each other
Can be created, modified, and torn down in software — no manual per-device config

## Slide 6
Key Network Metrics You Need to Know
Bandwidth
The amount of data that can be transmitted per second (Gbps = gigabits per second). Think of it as road width.
Latency
The time for a packet to travel from source to destination (milliseconds). Think of it as travel time.
Jitter
Variation in latency. Even low latency is useless for video calls if it varies wildly packet-to-packet.
Blocking
A connection request is "blocked" when the network cannot accommodate it due to insufficient resources.
SLA
Service-Level Agreement — a contract defining the minimum performance the network must deliver to a tenant.
Utilization
Fraction of capacity currently in use. High utilization = efficient but risky. Low = wasteful but safe.

## Slide 7
Activity 1
Think-Pair-Share
You use the internet every day. Think about two apps you use — one that needs fast response time and one that just needs to download a lot of data.
1 min — Think
Individually: name one app that needs low latency (feels laggy if slow) and one that needs high bandwidth (needs to move a lot of data). What would break first if each got congested?
2 min — Pair
Compare with the person next to you. Did you pick the same apps? Which requirement — latency or bandwidth — do you think is harder for the network to guarantee?
2 min — Share
One pair shares with the class.

## Slide 8
Part 2: Virtualization & NFV
From dedicated hardware boxes to software running on commodity servers

## Slide 9
The Old Way: Dedicated Hardware Per Function
For decades, each network function ran on its own proprietary physical appliance. Want a firewall? Buy a firewall box. Want load balancing? Buy a load balancer. This is expensive, slow to deploy, and impossible to scale flexibly.
🔒
Firewall
⚖️
Load
Balancer
🔍
Deep Packet
Inspection
🔄
NAT
Gateway
📡
WAN
Optimizer
Cost
Each box costs tens of thousands of dollars
Vendor lock-in for every function
Spare hardware sits idle
Speed
Procurement takes weeks to months
Configuration is manual and error-prone
Cannot spin up a new function in minutes
Flexibility
Hard-coded to one function
Cannot share compute with other tasks
Scaling means buying more boxes

## Slide 10
Network Function Virtualization (NFV)
NFV moves network functions from proprietary hardware into software — called Virtual Network Functions (VNFs) — running on commodity servers.
BEFORE: NFV
AFTER: NFV
📦 Firewall box
📦 Load balancer box
📦 IDS/IPS box
📦 NAT box
→
Commodity Server
⚙ vFirewall
⚙ vLoad Balancer
⚙ vIDS/IPS
⚙ vNAT
VNFs can be instantiated, scaled, migrated, or deleted in seconds — entirely in software.

## Slide 11
Part 3: Network Slicing
Carving isolated virtual networks from shared physical infrastructure

## Slide 12
What Is a Network Slice?
A network slice is an end-to-end logical network built on top of a shared physical infrastructure — with its own dedicated virtual resources and SLA.
Physical Layer — Routers · Fiber Links · Servers · Radio Towers
eMBB Slice
(High-speed video)
URLLC Slice
(Autonomous cars)
mMTC Slice
(IoT sensors)
Slice Layer
Key guarantee: a failure or overload in one slice does NOT affect other slices.
Slice Layer
Slice Layer

## Slide 13
Activity 2
Which of the following best describes a network slice?
A
A physical cable running between two data centres
B
A software patch applied to a router to improve its speed
C
A logically isolated virtual network carved from shared physical infrastructure, with its own guaranteed SLA
D
A VLAN tag added to Ethernet frames to separate broadcast domains
💬 Discuss with your neighbour before answering. 30 seconds.

## Slide 14
Activity 2 — Answer
Which of the following best describes a network slice?
A
A physical cable running between two data centres
B
A software patch applied to a router to improve its speed
C
A logically isolated virtual network carved from shared physical infrastructure, with its own guaranteed SLA
D
A VLAN tag added to Ethernet frames to separate broadcast domains
✓ C — A slice is end-to-end, virtual, isolated, and SLA-guaranteed. VLANs (D) only separate broadcast domains at Layer 2 — no dedicated resources, no lifecycle management.

## Slide 15
What Makes a Slice Different from a VLAN?
VLANs provide basic traffic separation. Network slices go much further — they are complete end-to-end virtual networks.
Property | VLAN (Virtual LAN) | Network Slice
Scope | Layer 2 only (Ethernet) | End-to-end: radio + transport + core + compute
Resources | Shared, best-effort | Dedicated, guaranteed per SLA
Functions | None — just switching | Full set of VNFs per service class
Isolation | Traffic separation only | Full resource and failure isolation
Management | Static VLAN IDs | Dynamic lifecycle: create, scale, tear down
A network slice is essentially a private, end-to-end virtual mobile network — complete with its own VNFs, topology, and SLA.

## Slide 16
5G and the Three Slice Classes
The 3GPP standard for 5G defines three canonical service categories, each requiring a fundamentally different network behavior.
eMBB — Enhanced Mobile Broadband
Smartphones, 4K/8K video, AR/VR headsets
Requires: very high bandwidth (up to 20 Gbps peak)
Latency-tolerant: 10–50 ms is fine
Challenge: allocating bandwidth efficiently during peak hours
URLLC — Ultra-Reliable Low-Latency Comms
Autonomous vehicles, remote surgery, factory automation
Requires: < 1 ms end-to-end latency
Reliability: 99.9999% packet delivery
Challenge: guaranteeing hard real-time in a shared network
mMTC — Massive Machine-Type Communications
IoT sensors, smart meters, agricultural monitors
Requires: supports millions of devices per km²
Very low data rate per device (bytes/hour)
Challenge: connection density, not raw speed

## Slide 17
ACTIVITY 3
Match the Application to Its Slice Class
Draw a line connecting each application on the left to the correct 5G slice class on the right.
Live 4K sports stream on your phone
Smart electricity meter reporting usage every hour
Surgeon remotely operating a robot from 200 km away
Nightly cloud backup of your company's database
Thousands of soil sensors in a smart farm
VR headset in a crowded stadium
eMBB
High bandwidth
low latency-tolerance
URLLC
Ultra-low latency
high reliability
mMTC
Massive device count
low data rate
✎ Write your answers on paper or discuss in pairs.

## Slide 18
ACTIVITY 3 — Answers
Correct Matches
Live 4K sports stream
→
eMBB — high bandwidth needed
Smart electricity meter (hourly)
→
mMTC — low rate, massive scale
Remote robot surgery
→
URLLC — < 1 ms, 99.9999% reliability
Nightly cloud backup
→
eMBB — bulk throughput, delay-tolerant
Soil sensors in smart farm
→
mMTC — many devices, tiny data
VR headset in stadium
→
eMBB — very high bandwidth per device
Note: cloud backup maps to eMBB (bulk throughput) — not mMTC. mMTC is about massive numbers of devices, not large file sizes.

## Slide 19
Part 4: Service Function Chains
Ordered pipelines of virtual network functions

## Slide 20
Service Function Chains (SFCs)
A Service Function Chain is an ordered sequence of Virtual Network Functions that a traffic flow must traverse — from source to destination.
Traffic
Source
🔒
Firewall
⚖️
Load
Balancer
🎬
Transcoder
🔍
DPI
Traffic
Dest
Each VNF processes the traffic and passes it to the next function in the chain.
Why Ordering Matters
Firewall must run before load balancer (malicious traffic should be dropped first)
Transcoding must run before encryption (cannot transcode encrypted data)
Wrong order = security holes or wasted compute
SFC + Slicing Together
Each network slice hosts one or more SFCs
Different slices can have entirely different SFC topologies
The mapping of SFC to physical resources is the "slice embedding" problem
Resource Requirements
Each VNF needs: compute (CPU/RAM) at a node
Each link between VNFs needs: bandwidth
End-to-end: latency budget must not be exceeded

## Slide 21
The Slice Embedding Problem
Given a slice request (topology + resource requirements), how do we map it onto the physical network? This is an NP-hard optimization problem.
Slice Request Arrives
Find Feasible Path(s)
Place VNF Instances
Allocate Bandwidth
Accept or Reject
What We Must Decide
Which physical nodes host each VNF (compute placement)
Which physical links carry each virtual link (routing)
How much bandwidth to allocate on each link
Which path to use when multiple exist (k-shortest paths)
Constraints to Satisfy
Node capacity: compute at each physical node is finite
Link capacity: bandwidth on each link is finite
Latency: total end-to-end delay must meet SLA
Availability: redundancy required for critical slices
The decision is made once at admission time. Getting it wrong wastes resources or violates SLAs — neither is acceptable.
Key Trade-off: Acceptance Rate vs Resource Efficiency
Accepting more requests increases revenue — but also increases congestion and the risk of future blocking

## Slide 22
Part 5: Elastic Traffic
When bandwidth demand is not fixed — it fluctuates

## Slide 23
Static vs Elastic Traffic Models
Most early slice research assumed static traffic — a slice consumes a fixed bandwidth for its entire lifetime. Real workloads do not behave this way.
Static Traffic (Simple)
Bandwidth is fixed at slice setup time
E.g., a 10 Gbps video stream that always uses 10 Gbps
Admission control is straightforward: check if 10 Gbps is available
Resource reservation is simple: hold 10 Gbps for the slice lifetime
Research tool: LP (Linear Programming) to minimize cost
Limitation: Underestimates the complexity of real workloads
Elastic Traffic (Realistic)
Bandwidth alternates between a BASE level and a PEAK level
Slice is normally at base — then bursts to peak on demand
The network cannot predict exactly when the burst will happen
Example: enterprise sync (base) → nightly backup (peak)
Example: cell tower (base) → concert crowd surge (peak)
Challenge: how many elastic slices can safely share a link?
Elastic traffic is more efficient but introduces a new risk: if too many slices burst simultaneously, none of them can reach peak — a "peak-state blocking" event.

## Slide 24
Modeling Elastic Slices: Continuous-Time Markov Chain
Each accepted slice request independently transitions between BASE and PEAK state. We model this with a CTMC — a probabilistic model of state transitions over continuous time.
Steady-State Probabilities
π_peak = λbp / (λbp + λpb) = 5/15 = 1/3
π_base = 2/3
At any instant: roughly 1/3 of all active slices are in PEAK state
This fraction fluctuates — it cannot be predicted with certainty
The unpredictability is the root cause of peak-blocking under high load
Why This Makes Admission Hard
Each new slice you admit adds future peak demand to every link on its path
That demand materializes at a random future time — not now
The more slices you admit, the higher the risk of simultaneous peak bursts
A greedy "accept everything" policy leads to catastrophic blocking under load

## Slide 25
Peak-State Blocking: The Core Problem
A peak-state blocking event occurs when an active slice tries to upgrade to peak bandwidth — but the network cannot accommodate it.
Timeline example: 4 slices sharing a 100 Gbps link
Link capacity: 100 Gbps
Slice A
Base 20 Gbps
→ tries to burst to Peak 40 Gbps
✓ succeeds
Slice B
Base 20 Gbps
→ tries to burst to Peak 40 Gbps
✗ BLOCKED (only 40 Gbps left after A)
Slice C
Base 20 Gbps
→ stays at base
Slice D
Base 20 Gbps
→ stays at base
Why this is expensive
Peak bandwidth commands premium pricing — 5–10× the rate of base service.
Blocking peak = direct revenue loss + SLA breach.

## Slide 26
ACTIVITY 4
Is This Network in Trouble?
Work through the scenario below with your neighbour. All calculations can be done mentally.
Scenario
A single 100 Gbps fiber link carries 12 accepted elastic slice requests. Each request uses 5 Gbps at base state and 10 Gbps at peak state. The base→peak transition rate λbp = 5.0 and peak→base rate λpb = 10.0.
Q1
What is the steady-state probability that any one slice is in the peak state? (Recall: π_peak = λbp / (λbp + λpb))
Q2
On average, how many of the 12 slices are simultaneously in peak state?
Q3
If all 12 slices happened to burst at the same time, how much bandwidth would be needed? Would the link survive?
Q4
Should the operator accept a 13th request? What additional information would you want to know?

## Slide 27
ACTIVITY 4 — Answers
Is This Network in Trouble? — Worked Answers
Q1
π_peak = 5.0 / (5.0 + 10.0) = 5/15 = 1/3 ≈ 33%
Q2
Expected simultaneous peak = 12 × 1/3 = 4 slices in peak state on average
Q3
All 12 peak simultaneously: 12 × 10 Gbps = 120 Gbps > 100 Gbps link capacity. The link would be overloaded — 12 simultaneous peaks is a worst-case scenario, but it CAN happen.
Q4
A 13th request adds more peak risk. Need to know: current number of slices already in peak state, per-link utilization across the path, and the expected revenue vs. blocking penalty trade-off. This is exactly the admission control problem RL solves!

## Slide 28
Part 6: Admission Control & Our Lab Work
How an RL agent learns to accept or reject slice requests

## Slide 29
Four Strategies for Elastic Slice Admission Control
Our lab compared four approaches across a wide range of arrival rates on the 14-node NSFNet topology.
No Admission
Control
Accept any request that fits at the base level. No peak bandwidth reserved. Simple, but peak blocking explodes under load.
Reservation
Heuristic
Reserve full peak bandwidth at admission time. Zero peak blocking guaranteed — but acceptance rate crashes because capacity is locked out.
Dynamic
Threshold (60%)
Reject requests when per-link utilization exceeds 60%. Simple gate — but ignores mix of base/peak requests and cannot adapt to load changes.
RL Admission
Control (PPO)
A trained agent observes the full 51-dimensional network state and learns a load-adaptive accept/reject policy. Our proposed approach.
The fundamental tension: accepting more = more revenue now but more peak blocking later. RL learns to balance this dynamically.

## Slide 30
The RL Agent: How It Works
We frame admission control as a Markov Decision Process (MDP) and train an agent using Proximal Policy Optimization (PPO).
Network
Environment
State
Observation
(51-dim)
PPO
Policy
Agent
Accept /
Reject
Reward
Signal
← Feedback: reward shapes future policy
State Vector (51 dims)
Per-link utilization — total and base-only — for all 21 NSFNet links (42 values)
Request features: source, destination, path length, arrival rate (7 values)
System occupancy: normalized base-state and peak-state request counts (2 values)
Reward Function
Revenue on departure: +proportional to bandwidth × time served at base and peak
Peak blocking penalty: −40 per blocked BTP event
Congestion penalty: exponentially growing negative signal when avg utilization > 40%
Training Setup
Algorithm: PPO with clip ratio 0.2
Policy network: 2-layer MLP, 256 units each, ReLU
Training: 200k timesteps at λ=20, then fine-tuned per evaluation rate
Topology: 14-node NSFNet, 100 Gbps per link

## Slide 31
Results: RL vs Baselines
Evaluated across arrival rates λ ∈ [1, 50] req/unit-time on the NSFNet topology. Key findings at high load (λ = 50):
↓ 3×
RL peak blocking vs No Admission at λ=50 (15% vs 45%)
↑ 127%
RL net revenue vs No Admission at high load ($295k vs $130k)
< 1%
Capacity-based rejection under RL — links never saturate
Strategy | Peak Blocking | Net Revenue (λ=50) | Actual Utilization
No Admission | 45% | ~$130,000 | 54%
Dynamic Threshold (60%) | 35% | ~$228,000 | 51%
RL — Our Approach | 15% ✓ | ~$295,000 ✓ | 40% ✓
Reservation Heuristic | 18% | ~$305,000 | 43%
RL dominates No Admission and Dynamic Threshold at all moderate-to-high loads, and matches the Reservation Heuristic on peak blocking at λ ≥ 30 while requiring no upfront bandwidth reservation.

## Slide 32
ACTIVITY 5
Design Your Own Admission Policy
In groups of 3–4, imagine you are the network operator. You must decide a rule for accepting or rejecting incoming slice requests.
Your Network: 14-node topology · 100 Gbps per link · Requests arrive randomly, each wanting 5–15 Gbps base, 10–30 Gbps peak · Peak penalty is 4× worse than base rejection penalty
1
Write your rule:
In plain English: what condition must be met for you to say YES to a new request? E.g., "Accept if link utilization is below X% AND…"
2
Predict the weakness:
Every fixed rule has a failure case. When does your rule make the wrong decision — admitting a request it should reject, or rejecting one it should accept?
3
Compare strategies:
How does your rule compare to the four strategies in the seminar? Is it closest to No Admission, Reservation, Dynamic Threshold, or RL?
4
Pitch it:
30 seconds per group: state your rule and its biggest weakness. Class votes on which group's rule they'd trust with their own network.

## Slide 33
DISCUSSION 6
Reflect & Connect
Big Picture
The RL agent reduces peak blocking from 45% to 15% at high load — but it still blocks 15% of peak-state upgrades. Is 15% acceptable? What kind of service would you refuse to run on a network with 15% peak blocking?
Fairness Question
The RL agent's reward function maximizes net revenue — not fairness. Could it learn to reject requests from low-revenue slices to protect high-revenue ones? Is that a problem? How would you fix it?
Real World
Our RL agent was trained in simulation. What could go wrong when you deploy a simulation-trained agent on a real network? What information from the real world is NOT captured in our model?
Looking Ahead
Seminar 2 will add optical networks to the picture — the actual fiber links carrying your slices. How do you think optical constraints (like limited spectrum slots) will change the admission control problem?

## Slide 34
Seminar 1 — Key Takeaways
01. The Internet carries radically different traffic types that need different performance guarantees.
02. NFV virtualizes network functions as software on commodity servers — enabling flexible, software-driven networks.
03. Network slicing creates logically isolated virtual networks on shared physical infrastructure, each with its own SLA.
04. Service Function Chains define the ordered sequence of VNFs that traffic must traverse per service.
05. Elastic traffic fluctuates between a base and a peak bandwidth level — modeled as a two-state CTMC.
06. Our RL agent (PPO) learns a congestion-aware admission policy that cuts peak blocking 3× vs no admission, achieving up to 127% higher revenue at high load.
Next: Seminar 2 — Optical Networks (Fiber physics · WDM · SDM · RMCSA · VONE)